## Slide 1: Using Hyperpolarized 129Xe MRI to Detect Impaired Cerebral Perfusion in Human Brain with Alzheimer’s Disease
Tao Li1 , Francis T. Hane1,2 , Jane M. Lawrence-Dewar2 , Ayman Hassan3 , Karl Granberg3 , Raiili M. Pellizzari1 , Jennifer A. Plata1 , and Mitchell S. Albert1,2,4
1. Department of Chemistry, Lakehead University, Thunder Bay, ON, Canada,
2. Thunder Bay Regional Health Research Institute, Thunder Bay, ON, Canada,
3. Thunder Bay Regional Health Sciences Centre, Thunder Bay, ON, Canada,
4. Northern Ontario School of Medicine, Thunder Bay, ON, Canada.

## Slide 2: Faculty/Presenter Disclosure Slide
Tao Li
Relationships with commercial interests: NONE
Potential for conflict(s) of interest: NONE

## Slide 3: Introduction
Hyperpolarized (HP) xenon-129 (129Xe) MRI has long been used to study structural and functional information of the lungs.
Inhaled Xenon gas can dissolve in the blood and be carried to brain tissues by cerebral blood flow (CBF), this makes it potentially a powerful tool to probe the physiological and functional information of the brain.
Albert et al. Nature, 1994

## Slide 4: 129Xe Brain Study – Preclinical
Mazzanti et al. (2011)
Zhou et al. (2010)
Swanson et al. (1997)
HP 129Xe brain MRI studies have been conducted in animal models by numerus groups through the years.
Advanced brain studies such as stroke and fMRI using this technique have also been investigated.
Notes: Full References.

## Slide 5: 129Xe Brain Study - Human
129Xe human brain images have been acquired in recent years.
We have started to explore using HP 129Xe MRI as a tool to probe and assess physiological and functional changes in the brain.
Rao et al. (2015-2016)
Li et al. (2017)
Rao et al. (2017)

## Slide 6: Alzheimer’s Disease
Alzheimer’s Disease (AD) is a neurodegenerative disease and the leading type of dementia.
Diagnosis of AD largely relies on cognitive assessment combined with traditional MRI and CT to rule out other pathological changes in brain structure.
Quantitative assessment of AD can also be done with PET or SPECT, using a radiotracer that binds to the beta-amyloid plagues.
All at a stage when symptoms start to show.

## Slide 7: Study Rationale
Increasing evidence has shown that reduced CBF starts at an early, asymptomatic stage of AD.
Glucose uptake reduced due to degraded CBF in different stages of AD.
Binnewijzend et al. (2017) Eur Radiol. Feb;26(2):506-14.
Jack C. de la Torre (2017)
J Alzheimers Dis DOI 10.3233/JAD-161266
Can HP 129Xe MR detect the physiological changes at an early stage of AD?

## Slide 8: Methods – Dynamic Imaging
Images were dynamically acquired at 10s, 20s, and 30s from the start of a 20s-breathhold after the inhalation of 1L xenon gas.
Pulse Sequence | Views | FOV (mm) | Matrix | TR / TE (ms) | Flip angle (degree) | Bandwidth (Hz/pixel) | NSA
2D GRE | Sag./Ax. | 250 x 250 | 32 x 32 | 250 / 0.84 | 12 | 150 | 1

## Slide 9: Methods – Xenon Washout Spectroscopy
Our study was to measure xenon washout times in brain tissues and compare it between the healthy and AD group.
MR spectra were acquired at 2 seconds intervals, starting immediately after 500ml xenon gas inhalation.

## Slide 10: Methods – Clinical Study Design
Study participants:
    AD participants : n = 4, age 72 ± 7, MoCA score 21 ± 3,
    Healthy participants: n = 6, age 70 ± 5, MoCA score 28 ± 1.
Montreal Cognitive Assessment (MoCA) was used to assess the cognitive level of all participants.
This study protocol had been approved by Health Canada and local Research Ethics Boards.

## Slide 11: Methods - Hardware
Philips Achieva 3T clinical scanner.
CMRS Dual-Brain 129Xe - 1H dual-tuned quadrature coil.
Xemed SEOP xenon polarizer (enriched xenon-129 to 30% polarization).

## Slide 12: Results - 129Xe Dynamic Images
Sagittal
Axial
Healthy
AD
Three dynamics images were acquired in each view.

## Slide 13: Results - 129Xe Dynamic Images
SNR of each dynamic image was normalized with respect to that of the first one.
2nd dynamic
3rd dynamics
1H Localization
1st dynamic

## Slide 14: Results - 129Xe Dynamic Images
A slower decay of the signal were observed in AD participants, but it’s not statistically significant (p = 0.37).

## Slide 15: Results – High Resolution Spectroscopy
Four of five previously identified xenon peaks are well resolved.
The peak from interstitial fluid/CSF (199ppm) is barely observable.
No significant differences were found between the two groups.

## Slide 16: Results - 129Xe Wash-out
In both gray matter and white matter, xenon wash-out time is significantly longer in AD group than in the age-matched healthy group.
Gray Matter White Matter

## Slide 17: Xenon Washout Spectroscopy
The measured xenon washout signals were fitted to the following model:
where , and
is cerebral perfusion,
is Xenon partition coefficient,
T1 is xenon relaxation time in tissue.
Martin et al. J Magn Reson Imaging. 1997 Sep-Oct;7(5):848-54.

## Slide 18: Results - 129Xe Wash-out
The values derived from xenon wash-out time from the two groups were significantly different in both gray matter and white matter (p < 0.01), largely attributed to a degraded cerebral perfusion in AD group.
Notes: Use all data

## Slide 19: Discussion
Significantly different xenon wash-out times from the brain tissues of healthy and AD participants.
Resulted from degraded cerebral perfusion caused by AD.
T1 relaxation time of Xenon in brain tissues healthy group and the AD group could contribute to the difference.
A third compartment containing dissolved xenon can also lead to a different wash-out time.

## Slide 20: Conclusions
The study demonstrated that HP 129Xe MRI is potentially a sensitive bio-marker to probe physiological changes caused by AD, and possibly for other neurodegenerative diseases as well, at an early predementia stage.
Notes: New bio marker

## Slide 21: Acknowledgement
Dr. Seda Rafilovich
Dr. Alla Reznik
Dr. Ayman Hassan
R.Ts and MRI technicians at Thunder Bay Regional Health Science Center
Clinical MR Solutions, LLC
Xemed, LLC

## Slide 22: Thank you!